## Slide 1: Safety Management Systems
2026 Air Carrier Purchasing Conference
August 31, 2026

## Slide 2: Who is this Guy?
Aviation attorney since 1992
General Counsel to the Aviation Suppliers Association since 1997
Our law firm represents and counsels air carriers, manufacturers, repair stations and distributors
Worked with governments on developing SMS and worked with aviation businesses to establish SMS systems

## Slide 3: Learning Goals
Understand the basic structure of SMS
Understand how to use Safety Risk Management
Learn how Safety Risk Assessment functions
Learn some tips on how to make your own Safety Risk Management process valuable to your organization
Note: for more guidance, see FAA AC 120-92D

## Slide 4: SMS Is Not…
SMS will not be a drop-in replacement for your quality assurance system
  But it might coordinate and rely on your quality assurance system
SMS is not the last-best-system you will ever use
  There is always another system
  But SMS should stick around for awhile because of the upcoming regulations
SMS is not simple – it is a complicated structure of interlocking pieces
  But many of the system elements may already exist in your existing model
  If the pieces work together properly, then they can use their synergy to make this system even more valuable than the pieces

## Slide 5: We’ve All Got Quality Systems, Already …
Why should we care about SMS?
It is being required by regulations
  ICAO “mandated” it and established the “standard” for governments to follow
  FAA and EASA already require SMS for air carriers
  EASA is imposing SMS requirements on manufacturer and repair stations
    Compliance deadline is December 31, 2025
  FAA is relying on voluntary SMS for repair stations
    December 31, 2025 deadline applies for EASA-145 repair stations located in the United States

## Slide 6: Why Else Should We Care About SMS?
It can add safety value
It can add management tools to help management understand the organization’s safety posture
It can add management tools to help management understand the organization’s safety response
It can offer an improved mechanism for proactive management of risk
It can offer an improved mechanism for managing change
But to get these benefits,
you have to build an effective system

## Slide 7: SMS Looks a Bit Like QMS
In many ways, SMS is like a traditional Quality Management System (QMS) with some added safety analysis elements, and without some non-safety elements (like customer service) :
SMS
QMS
  SMS-Only Elements Like:
  Proactive Hazard Identification
  Formal Risk Assessment and Analysis
  QMS-Only Elements Like:
  Customer Satisfaction
  On Time Delivery
SMS overlaps with QMS and can rely on elements of QMS

## Slide 8: SMS Looks a Bit Like QMS; So Make Use of Your Existing QMS
In many ways, SMS is like a traditional Quality Management System (QMS) with some added safety analysis elements, and without some non-safety elements (like customer service)
This means that you can use your QMS as a foundation for SMS
  Reuse QMS processes, like hazard identification and corrective action
  Rely on QMS processes as mitigations (take credit for your existing systems)
SMS
QMS
SMS overlaps with QMS and can rely on elements of QMS

## Slide 9: SMS is Proactive
SMS identifies hazards and proactively assesses them to identify their risk level
  SMS invites scrutiny to identify hazards (without necessarily waiting for an occurrence to reveal the hazard)
  SMS proactively mitigates the risk of hazards to an acceptable level
  SMS uses Safety Assurance mechanisms and performance indicators to ensure that the mitigations are being successful

## Slide 10: Mitigating “Black Swan” Events
The problem with unpredictable events is that you cannot predict them
But you can predict (and mitigate) the types of hazards that could face the business
For example, few people predicted that Covid-19 would effectively shut down the world
But you could have predicted, and mitigated, a hazard of inability for staff to be able to reach the office (for any reason)

## Slide 11: The Four Components of SMS
Safety Policy
and Objectives
Safety
Assurance
Safety Risk
Management
Safety
Promotion

## Slide 12: Four Components
1. Safety policy and objectives 1.1 Management commitment 1.2 Safety accountability and responsibilities 1.3 Appointment of key safety personnel 1.4 Coordination of emergency response planning 1.5 SMS documentation | 3. Safety assurance 3.1 Safety performance monitoring and measurement 3.2 The management of change 3.3 Continuous improvement of the SMS
2. Safety risk management 2.1 Hazard identification 2.2 Safety risk assessment 2.3 Safety risk mitigation | 4. Safety promotion 4.1 Training and education 4.2 Safety communication

## Slide 13: Four Components: Each Has Elements
1. Safety policy and objectives 1.1 Management commitment 1.2 Safety accountability and responsibilities 1.3 Appointment of key safety personnel 1.4 Coordination of emergency response planning 1.5 SMS documentation | 3. Safety assurance 3.1 Safety performance monitoring and measurement 3.2 The management of change 3.3 Continuous improvement of the SMS
2. Safety risk management 2.1 Hazard identification 2.2 Safety risk assessment 2.3 Safety risk mitigation | 4. Safety promotion 4.1 Training and education 4.2 Safety communication

## Slide 14: Safety Policy and Objectives
1. Safety policy and objectives 1.1 Management commitment 1.2 Safety accountability and responsibilities 1.3 Appointment of key safety personnel 1.4 Coordination of emergency response planning 1.5 SMS documentation | 3. Safety assurance 3.1 Safety performance monitoring and measurement 3.2 The management of change 3.3 Continuous improvement of the SMS
Establishing your Safety Policy and Objectives is very important, and it is the place to start in building a new system, BUT we are going to focus on other elements in this presentation
Management commitment to safety
And the foundational elements that support that commitment

## Slide 15: Safety Risk Management
In this workshop we are going to focus on the value that Safety Risk Management can bring to your organization
1. Safety policy and objectives 1.5 SMS documentation | 3. Safety assurance 3.1 Safety performance monitoring and measurement 3.2 The management of change 3.3 Continuous improvement of the SMS
2. Safety risk management 2.1 Hazard identification 2.2 Safety risk assessment 2.3 Safety risk mitigation | 4. Safety promotion 4.1 Training and education 4.2 Safety communication
Identifying hazards and responding to them to reach an expected level of safety

## Slide 16: Safety Assurance
Safety assurance can be influenced by the safety risk management program
You may be able to rely on your existing quality audit system as a part of safety assurance (don’t be afraid to use what you already have!)
1. Safety policy and objectives 1.1 Management commitment 1.2 Safety accountability and responsibilities 1.3 Appointment of key safety personnel 1.4 Coordination of emergency response planning 1.5 SMS documentation | 3. Safety assurance 3.1 Safety performance monitoring and measurement 3.2 The management of change 3.3 Continuous improvement of the SMS
Auditing to ensure that the system works as expected and to improve the system
Managing Change

## Slide 17: Safety Promotion
This is also important to a complete SMS, but is outside the scope of our discussion today
1. Safety policy and objectives 1.1 Management commitment 1.2 Safety accountability and responsibilities 1.3 Appointment of key safety personnel 1.4 Coordination of emergency response planning 1.5 SMS documentation | 3. Safety assurance 3.1 Safety performance monitoring and measurement 3.2 The management of change 3.3 Continuous improvement of the SMS
 | 4. Safety promotion 4.1 Training and education 4.2 Safety communication
Using training and communication to reinforce the system

## Slide 18: Focusing on Safety Risk Management

## Slide 19: Safety Risk Management (In Summary)
Identify Hazards (proactively when possible)
Perform Safety Risk Assessment on each identified hazard
  This will yield a risk level for the hazard
  Compare the risk level to metrics established in the Safety Policy & Objectives
Mitigate any hazard whose safety risk is unacceptable

## Slide 20: How Do I Start?
Assuming you already have your SMS processes written down, how do you start applying SMS to your business?
Starting by identifying hazards can be the easiest way to see early results
One place to start is with the hazards you’ve already identified
  Identify the hazards that have already been mitigated by your quality system
  You can examine how your quality system has mitigated the risk of each of these hazards
  This lets you take credit for the quality system you already have
  Working from your existing quality processes allows you to start with a manageable project

## Slide 21: Value of Hazard and Mitigation Identification
If you have identified your hazards, identified their related mitigations, and catalogued this information so it can be searched, then you can use this as a change management tool, because you will see what hazards are mitigated by each of your existing processes

## Slide 22: A Simple Safety Risk Assessment
For each Hazard,
  Likelihood is given a number
  Consequence is given a number
  The two numbers are multiplied
  The product is your Risk value
Warning: just because we are assigning numbers does not make this a quantitative analysis. Typically, this is a qualitative analysis based on the discretion of the system owner
  To the extent we use numbers, the numbers are for comparison within your system and cannot be compared to numbers in another system

## Slide 23: Road Runner’s Hazard Log
For each Hazard,
  Likelihood is given a number
  Consequence is given a number
  The two numbers are multiplied
  The product is your risk value
Hazard | Consequence | Likelihood | Risk
Coyote hits Road Runner with falling safe | 5 | 3 | 15
Coyote explodes Road Runner with dynamite | 5 | 4 | 20
Coyote pushes Road Runner off cliff | 4 | 3 | 12

## Slide 24: Likelihood
We assign values to different likelihood levels
The purpose of this assignment is to rank more likely occurrences higher than less likely occurrences
We rank more likely occurrences higher in order to be able to prioritize them (over rare occurrences of equal consequence) for purposes of risk assessment
The different levels of likelihood should be tailored to reflect the break points that are relevant to your operations
If the likely risk of ALL hazards is “remote” then you MAY need some way to distinguish them
  Or you may be satisfied that they are all adequately mitigated
Remember, this next page is an example – your actual standards must be tailored to your system’s needs

## Slide 25: Likelihood Examples: US MIL STD-882
5 - Frequent - likely to occur frequently
4 - Probable – will occur several times in the life of system
3 - Occasional – Likely to occur some time in the life of the system
2 - Remote – Unlikely but possible to occur in the life of the system
1 - Improbable – So unlikely, it can be assumed that occurrence may not be experienced
For example, a hazard that is likely to occur some time in the life of the system is considered “occasional” and is assigned a likelihood value of 3

## Slide 26: Likelihood Examples: FAA Risk Management Handbook (Certification)
4 - Probable - likely to occur in lifetime of each system (> 10-5)
3 - Remote – Possible for each item, several items for system (< 10-5)
2 – Extremely Remote – Unlikely for each item, may occur in system (< 10-7)
1 – Extremely Improbable – So unlikely, it is not expected in the system (< 10-9)
For example, a hazard that is likely to arise less than once in 10,000,000 operations is “extremely remote” and is assigned a likelihood value of 2

## Slide 27: Consequence (Sometimes Called Severity)
We assign values to different consequence levels
The purpose of this assignment is to rank more dire consequences higher than less dire consequences
We rank more dire consequences higher in order to be able to prioritize them for purposes of risk assessment
You have to define consequences, and levels of consequences, consistent with your own business needs and expectations
  This also allows you to mitigate to the desired levels
  You may evolve these levels as your safety management system develops
I have offered proposed consequence levels that serve only as a starting place for your own definitions

## Slide 28: Proposed Consequences
Negligible safety effect.
Failure conditions that would have no effect on safety
  E.g. following instructions in the wrong order, but ascertaining that the order has no safety effect
Assign a value of 1

## Slide 29: Proposed Consequences
Minor. Failure conditions that would not significantly reduce system safety
  Minor failure conditions may include a slight reduction in safety margins or functional capabilities
  Minor failure conditions may include a slight increase in personnel workload (such as a routine work process change)
Assign a value of 2

## Slide 30: Proposed Consequences
Major. Failure conditions that would reduce the safety capability of the business, or of a customer, or the ability of personnel to cope with adverse conditions
  Significant reduction in safety margins or functional capabilities
  Significant increase in personnel workload
Assign a value of 3

## Slide 31: Proposed Consequences
Hazardous. Failure conditions that would reduce the capability of the business, safety of a customer, or the ability of personnel to cope with adverse safety conditions, including:
  A large reduction in your safety margins or functional capabilities (e.g. conditions that can permit improper maintenance)
  A reduction in your customer’s safety margins or functional capabilities (e.g. a quality escape)
  Physical distress or higher workload such that personnel cannot be relied upon to adequately manage safety
Assign a value of 4

## Slide 32: Proposed Consequences: Possible Definition for Your System
Catastrophic. Failure conditions that are expected to affect the operation of a component, part, or element such that it can no longer function as intended for the customer:
  A quality escape that prevents proper operation (e.g. because it was installed)
Assign a value of 5
Recognize that other systems might assign death or hull loss as the top level – I have chosen to create a top level that is broader in scope

## Slide 33: Risk Table
 |  | Consequence |  |  |  | 
 |  | No Effect (1) | Minor (2) | Major (3) | Hazardous (4) | Catastrophic (5)
Likelihood | Frequent (5) | 5 | 10 | 15 | 20 | 25
 | Probable (4) | 4 | 8 | 12 | 16 | 20
 | Occasional (3) | 3 | 6 | 9 | 12 | 15
 | Remote (2) | 2 | 4 | 6 | 8 | 10
 | Improbably (1) | 1 | 2 | 3 | 4 | 5

## Slide 34: Risk Table
 |  | Consequence |  |  |  | 
 |  | No Effect (1) | Minor (2) | Major (3) | Hazardous (4) | Catastrophic (5)
Likelihood | Frequent (5) | 5 | 10 | 15 | 20 | 25
 | Probable (4) | 4 | 8 | 12 | 16 | 20
 | Occasional (3) | 3 | 6 | 9 | 12 | 15
 | Remote (2) | 2 | 4 | 6 | 8 | 10
 | Improbable (1) | 1 | 2 | 3 | 4 | 5
Red (10+) – Unacceptable level of risk – must be mitigated
Yellow (5-9) – Analyze to weigh whether mitigation is necessary
Green (1-4) – Acceptable level of risk

## Slide 35: Risk Table
 |  | Consequence |  |  |  | 
 |  | No Effect (1) | Minor (2) | Major (3) | Hazardous (4) | Catastrophic (5)
Likelihood | Frequent (5) | 5 | 10 | 15 | 20 | 25
 | Probable (4) | 4 | 8 | 12 | 16 | 20
 | Occasional (3) | 3 | 6 | 9 | 12 | 15
 | Remote (2) | 2 | 4 | 6 | 8 | 10
 | Improbable (1) | 1 | 2 | 3 | 4 | 5
Correlate the risk levels to the company’s safety policy to identify what is acceptable and what is not acceptable
As the system matures, you can choose to mitigate other risk levels

## Slide 36: A More Mature Table
 |  | Consequence |  |  |  | 
 |  | No Effect (1) | Minor (2) | Major (3) | Hazardous (4) | Catastrophic (5)
Likelihood | Frequent (5) | 5 | 10 | 15 | 20 | 25
 | Probable (4) | 4 | 8 | 12 | 16 | 20
 | Occasional (3) | 3 | 6 | 9 | 12 | 15
 | Remote (2) | 2 | 4 | 6 | 8 | 10
 | Improbable (1) | 1 | 2 | 3 | 4 | 5
In this more mature version of the table, items that were previously yellow (5-9 range) are now unacceptable, because the business has the resources to consistently mitigate the level 5-9 risks

## Slide 37: Let’s Try to Use these Values

## Slide 38: Building a New System
Hazard: The business could receive raw materials that do not meet the expected physical parameters
  For purposes of this exercise this can include counterfeit materials, non-conforming materials, materials damaged in transit, etc.
  But in a real system you might want to distinguish each of these as a different but related hazard

## Slide 39: Building a New System
Hazard: The business could receive raw materials that do not meet the expected physical parameters
Risk Assessment
  Likelihood – average (3)
  Consequence – catastrophic (5)
  “Product” = 15

## Slide 40: Building a New System
Hazard: The business could receive raw materials that do not meet the expected physical parameters
Risk Assessment
  “Product” = 15
Compare to the business’ Safety Policy (for our purposes, Safety Policy includes a requirement to mitigate all risk to 9 or less)
  A value of 15 represents an unacceptable risk

## Slide 41: Building a New System
Hazard: The business could receive raw materials that do not meet the expected physical parameters
Risk Assessment
  “Product” = 15
  A value of 15 represents an unacceptable risk
Next step: Mitigate the risk

## Slide 42: Starting to Record Hazards
Regulations and industry standards can be excellent sources of hazards and mitigations to start populating your hazard log
§ 21.137 Quality system.
  …. This quality system must include:
    Supplier control. Procedures that -
    (1) Ensure that each supplier-provided product, article, or service conforms to the production approval holder's requirements; ….
§ 145.211(c) Quality Control System
A certificated repair station must prepare and keep current a quality control manual in a format acceptable to the FAA that includes the following:
  (1) A description of the system and procedures used for -
    (i) Inspecting incoming raw materials to ensure acceptable quality;
    (ii) Performing preliminary inspection of all articles that are maintained;

## Slide 43: Mitigate the Risk
There are many mitigation strategies (and a full discussion of these is beyond today’s scope)
In our hypothetical (business could receive raw materials that do not meet the expected physical parameters), we might decide:
  To create a written receiving inspection system
  To hire dedicated receiving inspectors
  To train the receiving inspectors (initial and recurrent)
Each of these should be recorded as a mitigation connected to the hazard

## Slide 44: Record Your Results (details are examples, only)
Hazard
Detailed Information
Mitigation
Mitigations
Scope Limiters
Pointer to the Mitigation
Processes
Training
Hazard Description
Physical plant
Risk Assessment Details
Mitigation
Mitigations
Processes
Training
Physical plant
I like to do this in a relational database

## Slide 45: Management Tool
The SRM database (also know as a hazard log) permits creation of management tools, like a dashboard to easily identify safety hazards and the status on mitigating each identified hazard
Hazard | Original Conseq. | Original Likelihood | Original Risk | Mitigated Conseq. | Mitigated Likelihood | Mitigated Risk
Coyote hits Road Runner with falling safe | 5 | 3 | 15 | 5 | 1 | 5
Coyote explodes Road Runner with dynamite | 5 | 4 | 20 | 5 | 2 | 10
Coyote pushes Road Runner off cliff | 4 | 3 | 12 | 2 | 2 | 4

## Slide 46: Use Your SRM Information to Drive Safety Assurance (details are examples, only)
Hazard
Detailed Information
Mitigation
Mitigations
Safety Assurance
How will you review this?
Risk Assessment Details
Pointer to the Mitigation
Processes
Training
Hazard Description
Process Audits
Quality Control
Personnel Testing
Physical plant
Mitigation
Mitigations
Safety Assurance
How will you review this?
Processes
Training
Process Audits
Quality Control
Personnel Testing
Physical plant
Safety Assurance should ensure:
Mitigations are properly implemented, and
Anticipated results are realized

## Slide 47: Change Management
This record becomes a change management tool
Planning to change a procedure?
  Identify the hazards it mitigates in your records
  Identify how the change could affect the underlying hazards
  If the change affects the way that hazards are mitigated, then consider revising the anticipated change, or developing alternative mitigations, to reduce unintended consequences
Be sure to use your Safety Assurance mechanisms to ensure that the procedure change yields the expected results

## Slide 48: Conclusions
SMS is a tool for managing risk
SMS is becoming a regulated system
SMS can be used with your traditional quality system
Safety Risk Management is a part of SMS that we can use to assess risks associated with identified hazards
Safety Risk Management can be a safety-and-compliance tool in an aerospace organization

## Slide 49: Thank You
Jason Dickstein
Aviation Suppliers Association General Counsel
Washington Aviation Group
2233 Wisconsin Avenue, Suite 503
Washington, DC 20007
Tel: (202) 628-6776
Jason@WashingtonAviation.com